## Slide 1: Architecture
Changelog
Revision (Date) | Changes | Author
V0.2 (10.08.2017) | Initial version | ASI
V0.2 (13.08.2017) | OBC: Added bootloader selection connection | ASI

## Slide 2: Definitions
Abbreviations
Module name | Acronym/Abbreviation
Electric power supply | EPS
Onboard computer | OBC
Communication/Radio module | COM
Magnetic torquer board | MTB
Modulating retro-reflector board | MRRB
Camera module | CAM
Umbilical connector | UC
Kill-switch | KS
Remove before flight switch | RBF
Solar cell bus/output | PV
Magnetic torquer (actuator) | MT
Analog input/output | AN
Power output | PWR
Digital input/output | DIG
Antenna-board | ANT-B
Antenna | ANT

## Slide 3: Definitions
SatBus
Cable
Legend
Func.
Rail
ANT
Supply rails are marked by orange background
Interface connections are marked by yellowish background
All connections to the SatBus are indicated by a dashed frame
All connections via cable are indicated by a solid frame
HF connections are indicated by olive background color

## Slide 4: Blockdiagram
System overview
EPS
OBC
MRRB
COM
MTB
Antenna
MRRs
Solarcells
Camera
GPIO, PWM
UART, GPIO
RS485
SPI, GPIO
Modulator output
HF coax, Burn wire output
Kill-switches
RBF

## Slide 5: Blockdiagram
+12V
System supply overview
OBC
MRRB
COM
MTB
Solarcells
Camera
+3.3V
PV-BUS
EPS
(inc. batteries)
8x PV
Supply rail | Max. current | Comment
+3.3 V | 1 A | 
+12 V | 0.25 A | 
PV-Bus | < 1 mA | Only for RTC backup

## Slide 6: Blockdiagram
OBC
MCU ATmega1280V-8AU
FRAM
FM28V100
RS485 SN65HVD72D
Current
MAX4372
SPI
PWM
JTAG
RS485
UART
RBF
GPIO
Gyro 2 BMG250
Mag 2 FXOS8700
Mag 1 MAG3110
Mag 2 AK09912C
Temp 1 TMP36
Flash TC58CVG2S0
VDD
MAX892
VDD
Parallel
SPI (USART3)
Soft-PWM
UART0
UART1
I2C
SPI
GPIO
Reset/GPIO
3.3V
RTC
PCA2129
GPIO
ADC
VPP
MAX892
VEE
MAX892
VCC
MAX892
VCC
VEE
VPP
GPIO
GPIO
VRTC
PV-BUS
CURRENT
MAX4372
UART
GPIO
UART2
+3.3V
Measured
supply
RS485
Booloader
selection
Watchdog & Supervision MC74HC4538

## Slide 7: Blockdiagram
EPS
GPIO
12V-Reset
GPIO 3.3V-Reset
SPI
GPIO ADC-EOC
PV-BUS
I
MAX4372H
Charging & supervision
12V Converter
Power-switch
Power-switch
Temp.
TMP36
Supply- supervision
I
MAX4372H
I
MAX4372H
ADC
+3.3V
+12V
3.3V Converter
PV1-8
I-12V-IN
I-12V-IN
3.3V-EN
12V-EN
+UB
PVs
+3.3V
+12V
+3.3V
+12V
SPI
I-3.3V-IN
KS1-2-Delayed
PV-BUS
PV-BUS
-UB
-UB
Temp.
I-PV-IN
EN/DIS
+UB
-UB
Power-switch
KS1-2
KS3-4
Batteries
2x parallel
ADC-EOC
-UB
+UB
GPIO BAT-OK
Temp.
BAT-OK
3V3-Res
12V-Res
I-PV-IN
GND
Power-switch
MPPTs
8x
+UB
30 Min Timer
KS3-4
KS1-2
KS3-4

## Slide 8: Blockdiagram
MTB
Driver MC74LCX244
PWM
GPIO
6x PWM
Coil X
Coil Y
VDD MAX892
Coil Z
Enable
VDD
3.3V
+3.3V
PWM
PWM
PWM

## Slide 9: Blockdiagram
COM module
ATMEGA128L
UART
COM1
GPIO COM1
VDD MAX892
3.3V
ANT-B
12V
RF-Module
VDD
Burn wires
Power-switches
UART
COM2
GPIO COM1
4x PGPIO
4x GPIO
COM1-UART
COM1-GPIO
SPI
50Ω-HF-Coax
+3.3V
5V Converter
OC-protection
+3.3V
+12V-Fused
+5V
Enable
OC-Indicator
RBF
RBF

## Slide 10: Blockdiagram
Antenna board
Impedance matching & balancing (may be integrated into coax cable)
50Ω-HF-Coax
ANT-B
ANT
50Ω-HF-Coax

## Slide 11: Block diagram
Science Module (MRR)